## Slide 1: Network Layer and Attacks

## Slide 2: Outline
The Role of the IP layer
IP Header
IP Fragmentation and Attacks
Routing
ICMP and Attacks

## Slide 3: Network Layer
IP and ICMP
Addressing, forwarding and routing
Deliver packets to the transport layer
Provide error detection and diagnostic capability
Best effort service
  Bandwidth guarantee – No
  No-loss guarantee – No
  Ordering – No
  Timing – No
  Congestion indication – No

## Slide 4: Packet Traversal

## Slide 5: IPv4 Header
Notes: Talk about each field of the IP header

## Slide 6: IP Header
Version: For IPv4, this is always equal to 4
Internet Header Length (IHL): measured in units of four-byte blocks, minimum value is 5 (20 bytes), maximum is 15 (60 bytes)
Total Length: entire packet size in bytes, including header and data. The minimum size is 20 bytes (header without data) and the maximum is 65,535 bytes
Time To Live (TTL): Linux (64), Windows (128)
Protocol: defines the protocol used in the data portion of the IP datagram. ICMP (1), TCP (6), UDP (17)

## Slide 7: TTL and How Traceroute Works
TTL = 1, 2, 3, …
At each router: TTL --
Packet discarded and trigger ICMP when TTL=0
Notes: Talk about how traceroute works

## Slide 8: Implement traceroute

## Slide 9: The Need for Fragmentation
Limit of packet size

## Slide 10: IP Header Fields for Fragmentation

## Slide 11: How IP Fragmentation Works
Identification: primarily used for uniquely identifying the group of fragments of a single IP datagram
Flags
  bit 0: Reserved; must be zero
  bit 1: Don't Fragment (DF)
  bit 2: More Fragments (MF). For fragmented packets, all fragments except the last one have the MF flag set (MF = 0 for last fragment, 1 for others)
Fragment Offset: measured in units of eight-byte blocks except for the last fragment (think about why?). The first fragment has an offset of zero. Maximum offset is (-1)*8 = 8191 * 8 = 65,528 bytes
IPv6 does not support fragment

## Slide 12: Scapy IP Class

## Slide 13: An Example
A datagram of 4000 bytes (20 bytes of IP header plus 3980 bytes of IP payload) arrives at a router and must be forwarded to a link with an MTU of 1500 bytes.
Fragment | Bytes | ID | Offset | MF Flag
1st fragment |  |  |  | 
2nd fragment |  |  |  | 
3rd fragment |  |  |  | 
ID
=333
offset
=0
flag
=0
length
=4000
Notes: 1st fragment: Bytes=1500 (1480+20), ID=333, offset=0, Flag=1
2nd fragment: Bytes=1500 (1480+20), ID=333, offset=185, Flag=1
3rd fragment: Bytes=1040 (1020+20), ID=333, offset=370, Flag=0

## Slide 14: Another Example
Packet
  ID field: 1000
  IP Payload size: 100 bytes (UDP)
  Break into 3 fragments, each with at most 40 bytes of payload

## Slide 15: Build Fragments Manually (1)
Fragment 1
Fragment 2

## Slide 16: Build Fragments Manually (2)
Fragment 3
Execution Result

## Slide 17: Attacks on IP Fragmentation

## Slide 18: Attack 1: Tie Up Target's Resources
Question: Can you use a small amount of bandwidth to tie up a target machine's significant amount of resource?
Hint: use 2 small packets to cause server to allocate 64KB of RAM

## Slide 19: Attack 2: Create a Super-Large Packet
Question: Can you create an IP packet that is larger than 65,535 bytes? (The Ping-of-Death Attack)

## Slide 20: Ping of Death Attack
Maximum offset of (-1)*8 = 65,528 bytes. This means that an IP fragment with the maximum offset should have data no larger than 7 bytes, or else it would exceed the limit of the maximum packet length
Notes: >>> pkt=IP(dst='10.0.2.134')/ICMP()/('X'*60000)
>>> send(fragment(pkt))
Change 60000 to 70000 to see the difference

## Slide 21: A Recent Ping of Death Vulnerability

## Slide 22: Attack 3: Create Abnormal Situation
Question: Can you create some abnormal conditions using "offset" and "payload size"? (Teardrop Attacks)

## Slide 23: Teardrop Attack
a denial-of-service (DoS) attack that involves sending fragmented packets to a target machine. Since the machine receiving such packets cannot reassemble them due to a bug in TCP/IP fragmentation reassembly, the packets overlap one another, crashing the target network device

## Slide 24: Routing (Forwarding) Table
Over 4 billion () IP addresses, so rather than list individual destination address, list range of addresses (aggregate table entries)
Longest prefix matching - when looking for routing table entry for given destination address, use longest address prefix that matches destination address

## Slide 25: Routing Rules
Question: What interface will be used to route packets to
  (1) 192.200.60.5?
  (2) 192.168.30.5?
  (3) 192.168.60.5?
Routing Entry | Packet 1 | Packet 2 | Packet 3
A: 0.0.0.0/0 dev interface-a |  |  | 
B: 192.168.0.0/16 dev interface-b |  |  | 
C: 192.168.60.0/24 dev interface-c |  |  | 
D: 192.168.60.5/32 dev interface-d |  |  | 

## Slide 26: Routing Example
Destination 200.23.22.161 which interface?
11001000.00010110.00010110.10100001
Destination 200.23.24.170 which interface?
11001000.00010111.00011000.10101010
Destination Address Range |  | Link interface
200.23.16.0/21 | 1001000.00010110.00010000 | 0
200.23.24.0/24 | 1001000.00010110.00011000 | 1
200.23.24.0/21 | 1001000.00010110.00011000 | 2
otherwise |  | 3
Notes: 200.23.16.0/21- 1001000.00010110.00010000
200.23.24.0/24- 1001000.00010110.00011000
200.23.24.0/21- 1001000.00010110.00011000
200.23.22.161 interface 0
200.23.24.170 interface 1

## Slide 27: Routing Table
internet
10.0.2.3
10.0.2.128
192.168.60.2
192.168.60.128
10.0.2.2

## Slide 28: Change Routing Table
Add/delete an routing entry to/from the routing table
Notes: Add routes on 10.0.2.3 to provide route to 192.168.60.0/24. There is no need to provide route on 192.168.60.2 to 10.0.2.0/24 as 192.168.60.128 is the default router

## Slide 29: Change Routing Table
Add/delete the default gateway

## Slide 30: How Are Routing Tables Configured
For routers
  Routing protocols, OSPF, BGP, etc.
For hosts
  DHCP
  Using default routers
  Manual configuration
  ICMP redirect messages

## Slide 31: Question
When do the destination IP address in the IP header and destination MAC address in the Ethernet header not represent the same computer?

## Slide 32: Reverse Path Filtering (Spoofing Prevention)
Reverse path filtering is a mechanism adopted by the Linux kernel, as well as most of the networking devices out there to check whether a receiving packet source address is routable
If the reply to a packet wouldn't go out the same interface this packet came in, then this is a bogus packet and should be dropped

## Slide 33: Reverse Path Filtering Experiment: Setup

## Slide 34: Reverse Path Filtering Setting in Ubuntu 20.04
On Ubuntu 20.04, by default, the reverse path filtering mechanism is only set to the loose mode
  0: no checking on the source address, and asymmetric routing is allowed
  1: Strict mode. Asymmetric routing is not allowed
  2: Loose mode. Asymmetric routing is allowed, but the source address of the packet is checked against the routing table to ensure it is routable through one of the interfaces (any interface)

## Slide 35: Problems Caused by Docker Container
Docker changes the source IP address of the spoofed packet to 10.9.0.1
Docker only does that if the spoofed source IP address comes from a virtual network created by docker (such as 192.168.60.0/24)

## Slide 36: Problems Caused by Docker Container
We can get around this problem by creating another interface on the router container called tun0 and assign 192.168.70.11 as its IP address
Notes: # ip tuntap add mode tun dev tun0
# ip addr add 192.168.70.11/24 dev tun0
# ip link set dev tun0 up

## Slide 37: Demo Code
Notes: Make sure the routing entries on the three VMs are correct

## Slide 38: Internet Control Message Protocol (ICMP)
ICMP is a network-layer protocol. There is no port number associated with ICMP packets
ICMP messages are contained within standard IP packets as if it were a higher-level protocol, however, ICMP is actually an integral part of IP
Send Error messages
Send Operational information

## Slide 39: ICMP Header
Checksum: two bytes field calculated from the ICMP header and data
Rest of Header: Four-bytes field, contents vary based on the ICMP type and code
Data: ICMP error messages contain a data section that includes a copy of the entire IPv4 header, plus at least the first eight bytes of data from the IPv4 packet that caused the error message

## Slide 40: Scapy ICMP Class

## Slide 41: ICMP Echo Request
The Identifier and Sequence Number can be used by the client to match the reply with the request that caused the reply
Source: wikipedia

## Slide 42: ICMP Echo Reply
The echo reply is an ICMP message generated in response to an echo request; it is mandatory for all hosts, and must include the exact payload received in the request
The identifier and sequence number must match those in the echo request
Source: wikipedia

## Slide 43: Captured ICMP Echo Request and Reply

## Slide 44: Smurf Attack
The name comes from the idea of very small, but numerous attackers overwhelming a much larger opponent
The Smurf attack is a distributed denial-of-service (DDoS) attack in which large numbers of Internet Control Message Protocol (ICMP) packets (with the intended victim's IP as the spoofed source IP) are broadcast to a computer network using an IP directed broadcast address
If the number of machines on the network that receive and respond to these packets is very large, the victim's computer will be flooded with traffic

## Slide 45: IP Directed Broadcast
IP broadcast address – 255.255.255.255 or netid.255
In IP directed broadcast, the router automatically translates directed broadcasts to physical broadcasts within your network. In other words, Layer 3 broadcasts to the IP broadcast address (10.0.2.255 for the subnet 10.0.2.0/24) are translated into Layer 2 broadcasts with an address appropriate for the interface (e.g., ff:ff:ff:ff:ff:ff for an Ethernet interface)

## Slide 46: Smurf Attack
Direct broadcast address
  Example: 192.168.60.255 for network 192.168.60.0/24

## Slide 47: ICMP Time Exceeded
Time Exceeded is generated by a gateway to inform the source of a discarded datagram due to the time to live (TTL) field reaching zero
A time exceeded message may also be sent by a host if it fails to reassemble a fragmented datagram within its time limit
Code: Time-to-live exceeded in transit (0), Fragment reassembly time exceeded (1)
Source: wikipedia

## Slide 48: ICMP Time Exceeded
Type: 11
Code:
  0: Time-to-live exceeded in transit
  1: Fragment reassembly time exceeded
TTL=10

## Slide 49: Captured ICMP Time Exceeded Packet

## Slide 50: ICMP Destination Unreachable
Type: 3
Code
  0: Destination network unreachable
  1: Destination host unreachable
  2: Protocol Unreachable
  3: Destination port unreachable

## Slide 51: ICMP Redirect
ICMP Redirect is a mechanism for routers to convey routing information to hosts
The ICMP Redirect message informs a host to update its routing information (to send packets on an alternative route)
If a host tries to send data through a router (R1) and R1 sends the data on another router (R2) and a direct path from the host to R2 is available (that is, the host and R2 are on the same local network), then R1 will send a redirect message to inform the host that the best route for the destination is via R2

## Slide 52: ICMP Redirect and Attacks
Notes: Explain when this type of ICMP message is sent

## Slide 53: ICMP Direct Header
Code: redirect for Network (0), redirect for Host (1)
IP address: the 32-bit address of the gateway to which the redirection should be sent
IP header and additional data is included to allow the host to match the reply with the request that caused the redirection reply
Source: wikipedia

## Slide 54: ICMP Redirect Attack Lab
Notes: When they are set, after the attack is successful, the malicious router will receive the ping packet, but the kernel of the malicious router detects that the sender should send its packet directly to 10.9.0.11, so it sends out an ICMP redirect message (you can see it from the printout by the ping command). That changes the route cache from 10.9.0.111 back to 10.9.0.11. Therefore, to prevent this from happening, we have to ask the malicious router not to send out such ICMP redirect messages. Setting those parameters to zero achieves this purpose.

## Slide 55: ICMP Redirect Experiment: Setup
Make 10.9.0.11 the default router
10.9.0.11’s default router is 10.9.0.1

## Slide 56: ICMP Redirect Experiment
10.9.0.5 can directly send to 10.9.0.1: trigger ICMP redirect
After redirection (check 10.9.0.5)

## Slide 57: ICMP Redirect Attack Demo
ICMP redirect messages will not affect the routing table; instead, it affects the routing cache
Entries in the routing cache overwrite those in the routing table, until the entries expire
To display and clean the cache contents, we can use the following commands
# ip route show cache
# ip route flush cache

## Slide 58: Spoofing ICMP Redirect Message
Attack result
Notes: According to the ICMP protocol, ICMP redirect message should contain a data section
that includes a copy of the entire IP header, plus at least the first eight bytes of data from the
IP packet that caused the redirect message. The data section is used by the host to see which
packet has caused the error message, so the recipient can know which route should be updated.
Moreover, on Ubuntu 20.04, the recipient of the ICMP redirect message will verify whether the
packet information enclosed in the data part is consistent with the packets that were sent out. If
not, the message will be dropped.

## Slide 59: MITM Attack By Spoofing ICMP Redirect
Redirect traffic to attacker’s machines
Make changes before sending the packets out
Similar to the MITM attacking using the ARP cache poisoning attack

## Slide 60: Which Filter to Use

## Slide 61: Questions
Can you use the ICMP redirect attack to redirect the gateway to a remote computer?
Can you launch the ICMP redirect attack from a remote machine?

## Slide 62: NAT: Network Address Translation
Notes: Use this diagram to explain how the NAT works. There are several level of private networks in this diagram, each one has a NAT server.
Iptables –t nat –A POSTROUTING –j MASQUERADE –o eth0

## Slide 63: Summary
The Role of the IP layer
IP Header
Routing
ICMP